 MeinEnigma Commands Quick Reference
Jeff Tranter <tranter@pobox.com>

For software version 0.93
Serial port settings: 38400 bps, 8n1, no hardware handshaking or software flow control.
Commands can be in upper or lower case and abbreviated to fewer letters (shown below in bold).
Keyboard input is not echoed.
A colon followed by arguments will set the value.
Entering alphabetic characters (A-Za-z) will input text to encrypt/decrypt. Enter spaces for grouping.

Keyboard Keys in Model Mode

C - toggle clock mode	K - toggle the keyboard and rotor click sounds
L - lamp test (turn on all displays and LEDs)	M - toggle Morse code output
O - odometer, show total number of characters	S - display serial number
T - toggle text to speech output	V - show software version

Serial Port Commands

?	Help, display list of available commands

!SETTINGS	Shows the current settings

!MODEL:[EN I|M3|M4]	Displays or sets Enigma model.

!UKW:[UKWA|UKWB|UKWC|UKWBT|UKWCT]	Displays or sets reflector.

!ROTOR:[1,2,3,4,5,6,7,8,G,B]	Display or set rotor. Specify 3 or 4 rotors, depending on model.

!RING:[A,B,C,D]	Displays or sets rotor rings. Specify 3 or 4 values, depending on model.

!PLUGBOARD:[AB CD EF GH]	Displays or sets plugboard. Specify up to 10 letter pairs.

!START:ABC	Displays or sets rotor start position. Specify 3 or 4 rotors, depending on model.

!GROUPSIZE:4|5|6	Displays or sets group size.

!SAVE:1-15	Save current settings. Settings 1-4 can be recalled by pressing the appropriate
rotor button on powerup.

!LOAD:1-15	Load a saved setting.

!LOGLEVEL:0-2	Display or set log level. Higher levels display more information.

!TIME:hhmmss	Display or set real-time clock (hours, minutes, seconds).

 A B C D E F G H I J K L M N O P Q R S T U V W X Y Z
01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26
Example of Decoding a Real Message
(taken from http://enigmaworldcodegroup.freeforums.net/thread/75/enigma-challenge-2016)

Encrypted message (Enigma model M3 with UKW B reflector):

[EWGC2016]
XTS WWK
YNUAL FXBLJ PVARC AUEFD IQKFE VYCXN FRBBE HJJAN JDCRI GMJZC MSTAL WFSPB
YUNFG UUDYL DZJIG XQCSK QPURI EKMVO PDWKG IXBLH RVLYQ LBAPT PWGNU UGINK
RWYYI IFCQC XZSRZ MDQBM JHUNY LVLXN OAEVZ WSVAT FTVZT YOECZ HEOTB UUAPG
UHIDK GMNGR ADTEO IISNA ZOHZC WJWNP HLCPH PBTOW

Entry from keysheet for 1 May 2016:
 ------------------------------------------------------------------------------
|Tag |Walzenlage|Ringstellung| Steckerverbindungen | Kenngruppen |
--------------------------------------------------------------------------------
| 01 | I V III | 24 21 05 | AT BG CN EP FI HQ JS KZ OU XY | VWX YNU GUJ GGB |

Set machine as follows:

Model: M3
Reflector: UKWB
Rotor: 1,5,3
Plugboard: AT BG CN EP FI HQ JS KZ OU XY
Rotor Rings: X U E (24 = X, 21 = U, 05 = E)
Set rotor positions to first key in message: XTS
Type second key of message: WWK, decrypts to JZU
Now set rotor positions to: JZU
Look at first group in message, YNUAL.
Confirm YNU is a valid keygroup for the day.
Ignore last two characters (AL).

Enter rest of message on keyboard:
FXBLJ PVARC AUEFD IQKFE VYCXN FRBBE HJJAN JDCRI GMJZC MSTAL WFSPB
YUNFG UUDYL DZJIG XQCSK QPURI EKMVO PDWKG IXBLH RVLYQ LBAPT PWGNU UGINK
RWYYI IFCQC XZSRZ MDQBM JHUNY LVLXN OAEVZ WSVAT FTVZT YOECZ HEOTB UUAPG
UHIDK GMNGR ADTEO IISNA ZOHZC WJWNP HLCPH PBTOW

Decrypts to:
WITHS OMEME SSAGE SCAPT UREDI NMAYO FNINE TEENF ORTYA SWEDI SHMAT
HPROF ESSOR SPENT TWOWE EKSTO DECIP HERED ANDRE VERSE ENGIN EERED ANEAR
LYVER SIONO FTHES IEMEN SANDH ALSKE TFIFT YTWOA LSOKN OWNAS THEGE HEIMF
ERNSC HREIB ERXWH ATWAS HISNA MEQUE STION MARKX

Adding spaces and punctuation:
WITH SOME MESSAGES CAPTURED IN MAY OF NINETEEN FORTY A SWEDISH MATH PROFESSOR SPENT TWO WEEKS TO DECIPHERED AND REVERSE ENGINEERED AN EARLY VERSION OF THE SIEMENS AND HALSKE T FIFTY TWO ALSO KNOWN AS THE GEHEIMFERNSCHREIBER. WHAT WAS HIS NAME?

Serial port session for above:

!MODEL:M3
%MODEL:M3

!GROUPSIZE:5
%GROUP:5

!UKW:UKWB
%UKW: UKWB

!ROTOR:1,5,3
%ROTOR: I - V - III

!RING:X,U,E
%RING: - X U E

!PLUGBOARD:AT BG CN EP FI HQ JS KZ OU XY
%PLUGBOARD: AT BG CN EP FI HQ JS KZ OU XY

!START:XTS
%START: - X T S

WWK
>JZU

!START:JZU
%START: - J Z U

FXBLJ PVARC AUEFD IQKFE VYCXN FRBBE HJJAN JDCRI GMJZC MSTAL WFSPB
>WITHS OMEME SSAGE SCAPT UREDI NMAYO FNINE TEENF ORTYA SWEDI SHMAT

YUNFG UUDYL DZJIG XQCSK QPURI EKMVO PDWKG IXBLH RVLYQ LBAPT PWGNU UGINK
>HPROF ESSOR SPENT TWOWE EKSTO DECIP HERED ANDRE VERSE ENGIN EERED ANEAR

RWYYI IFCQC XZSRZ MDQBM JHUNY LVLXN OAEVZ WSVAT FTVZT YOECZ HEOTB UUAPG
>LYVER SIONO FTHES IEMEN SANDH ALSKE TFIFT YTWOA LSOKN OWNAS THEGE HEIMF

UHIDK GMNGR ADTEO IISNA ZOHZC WJWNP HLCPH PBTOW
>ERNSC HREIB ERXWH ATWAS HISNA MEQUE STION MARKX